## Slide 1
Fantastic Joules:
Tracking Power
Reproducing a Modern Computer Networks Research Paper
Team: M. Umair, Muhammad Umair Hafeez, Ahmad Hafeez
Instructor: Sir Akmal

## Slide 2
Why Does This Matter?
DATA CENTER
1.5%
of the world's entire electricity output
Biggest Power Users
Routers are the 'traffic officers' of the web and consume the most energy in the network.
The Problem
We don't actually know if the energy labels on industrial routers are honest or accurate.

## Slide 3
Our 3 Simple Questions
Trust Datasheets?
Can we trust the official energy labels and specifications from major manufacturers like Cisco?
Trust Sensors?
Can we trust the internal power sensors built directly into the routing hardware to report accurately?
Predict Power?
Can we formulate a mathematical model to accurately predict how much power a router will use?

## Slide 4
Where Did Data Come From?
CIRCUIT BOARD
10
Months
of real-world operational data from a Swiss Internet Provider (Switch)
777
Router Models
analyzed across the extensive study encompassing diverse hardware
1
Autopower Device
Custom Raspberry Pi device to measure the absolute truth of power usage

## Slide 5
Discovery 1: The False Labels
Router Model
Label (Typical)
Actual (Measured)
Difference
Cisco ASR 9000
1200 W
1728 W
+44.0%
Juniper MX960
2100 W
2150 W
+2.3%
Huawei NE40E
900 W
915 W
+1.6%
Conclusion: Manufacturers give "typical" power numbers on stickers. These labels are strictly for planning safe electrical cables, not for tracking real-world energy efficiency.

## Slide 6
Discovery 2: The Lightbulb Analogy
Chart: Time (24 Hours)
| 0h | 3h | 6h | 9h | 12h | 15h | 18h | 21h | 24h
Power Draw (Constant) | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Network Traffic | 15 | 30 | 25 | 55 | 75 | 60 | 80 | 55 | 70
Key Insight
Routers are like lightbulbs — once plugged in, they draw maximum power regardless of traffic load.
More traffic = more power?
WRONG.
Whether 1 or 1 million users are on the link, the power stays almost exactly the same.

## Slide 7
Discovery 3: No Link Sleeping
STREETLIGHTS STAY ON
Proposed Solution
"Link Sleeping" — turning off specific network ports at night to save power.
The Fact
The physical hardware plug (the "Transceiver") keeps drawing power even if the software port is set to "Off."
The Analogy
Closing a highway lane doesn't save energy if all the streetlights stay on anyway.

## Slide 8
How We Rebuilt the Experiment
The Setup
We created a clean environment using the exact ETH Zurich code within a Virtual Lab (Conda) to ensure consistency.
The Fix
We discovered a hidden bug in the original authors' code — a missing scipy library dependency — and successfully fixed it.
The Workaround
Since some raw data was missing, we engineered a custom script to extract high-resolution charts directly from the research PDF.

## Slide 9
Our Reproduction Success
Matched the Paper: Yes, our rebuilt models corroborated the authors' original findings.
Data Replication: Our independent calculations for Table 1 matched the paper perfectly.
Visual Validation: Our Figure 1 time-series analysis matched the paper's charts exactly.
Myth Busted: "Power vs. Traffic" is a myth at the network scale — successfully validated.

## Slide 10
9%
TOTAL ENERGY SAVED
How to Actually Save Energy
Focus on Hardware, not Software
Instead of attempting ineffective software solutions like turning off links, the focus should be on the Power Supply Units (PSUs).
Titanium Standard PSUs
Upgrading infrastructure to use more efficient power supplies meeting the Titanium standard can save 9% of total network energy instantly, without changing a single software setting.

## Slide 11
Questions?
Summary: Datasheets are unreliable; static power is the main enemy;
better plugs (Titanium PSUs) are the true solution.
Thank you for your time and attention!